## Slide 1
An Overview of IoT Applications In Agriculture with Two Case Studies Done Locally In Iran
Professor: Mohammad Hossein Bateni
Presented by: Mahdi Shirazi

## Slide 2
Mahdi Shirazi
Kiana Mahdian
Yasmin Torki
Group Members

## Slide 3
Introduction
Core Technologies and Architecture of IoT
IoT and Enabling Technologies in Precision Agriculture
IoT Applications In Agriculture
Case Study 1
Case Study 2
Conclusion
Discussion Structure
Topics we will tackle

## Slide 4
Introduction
  The Internet of Things (IoT) represents a significant technological advancement that interconnects everyday objects through the Internet, enabling them to send and receive data.
  Precision agriculture leverages IoT to optimize agricultural practices by using data from various sensors to monitor and manage environmental conditions, machinery, and irrigation systems.
  Two studies done in coordination to Iran’s agriculture are discussed.
4/32

## Slide 5
Core Technologies and Architecture of IoT
  IoT refers to a network of interconnected objects with sensors enabling internet connectivity.
Three-Layer IoT Architecture based on IEEE P2413 standard:
  Application Layer: Interfaces with end users and applications.
  Networking and Communication Layer: Handles connectivity and data transmission.
  Sensing Layer: Collects data through various sensors.
5/32

## Slide 6
Key IoT Technologies
  RFID: Uses radio waves to transmit data from mobile entities to readers.
  Identification Technologies: EPC and uCode for recognizing and addressing devices.
  Addressing Methods: IPv6 and 6loWPAN-IPv4 for connectivity.
  Communication Technologies: WiFi, ZigBee, Bluetooth, LTE, and 5G.
6/32

## Slide 7
IoT and Enabling Technologies in Precision Agriculture
IoT Hardware Platforms
Growth Drivers: Small, inexpensive microcontrollers and computing hardware.
Components: Processors, wireless chips, memory, and more.
  Arduino Mega
  Arduino Uno
  Arduino Yun Beaglebone Black
  Raspberry Pi3 (B model)
  Intel Galileo
7/32

## Slide 8
  Major Providers: AWS IoT, Microsoft Azure IoT Hub, IBM Watson IoT, Google Cloud, Salesforce IoT.
  Benefits: Scalability, affordability, extensive reach.
  Usage: Monitoring, control systems, data analysis, and planning.
The IoT cloud platforms in the context of agriculture
8/32

## Slide 9
  Definition: Automated exchange of information between devices with minimal human intervention.
  Technologies: IP, WiFi, SMS, Zigbee.
  Applications: Connecting agricultural machinery and vehicles, remote monitoring.
  Popular Apps: Sirrus, Manure Monitor, Agrivi, TractorPal.
Machine To Machine (M2M) communications in agriculture and Agricultural Smartphone Apps
9/32

## Slide 10
Internet of Things applications in agriculture
Precision Agriculture (PA) Overview
  A modern management approach using advanced technologies to enhance farming efficiency and productivity.
Key Technologies in PA:
  Information Technology (IT)
  Geographic Information Systems (GIS)
  Global Positioning Systems (GPS)
  Wireless Sensor Networks (WSN)
  Data Collection Techniques
Objectives of PA:
  Increase Crop Yields: Optimize inputs and farming practices.
  Minimize Environmental Impact: Reduce waste, conserve resources, and promote sustainability.
10/32

## Slide 11
Environmental Monitoring and Control
  Wireless Sensor Networks (WSNs): Scalability, fault tolerance, energy efficiency, effective monitoring systems.
  Key Parameters: WSN’s sensor nodes can measure and process several environmental parameters e.g. soil moisture, temperature, humidity, water pH, wind speed
  Advancements: Greenhouse monitoring, automated controls, data analysis via cloud.
11/32

## Slide 12
Ecological Monitoring
  Challenges: Environmental pollution, climate change, biological alterations.
  EIoT: Sensing, collecting, preprocessing, transmitting environmental data.
  Benefits: Continuous, real-time monitoring.
12/32

## Slide 13
Smart Irrigation Systems
  Water Demand: Agriculture accounts for 70% of global water consumption.
  Modern Systems: Networked sensors, microcontrollers, actuators.
  Implementation: Soil moisture sensors, data analysis, automated irrigation.
13/32

## Slide 14
Predicting the Impact of Internet of Things on the Value Added for the Agriculture Sector in Iran Using Mathematical Methods
Case Study 1

## Slide 15
Introduction
  Context: Iran faces significant water shortages, exacerbated by climate change, inefficient management, and excessive consumption.
  Objective: To investigate the economic impact of implementing IoT technology, specifically smart irrigation, in Iran's agriculture sector.
15/32

## Slide 16
Background on Iran's Agriculture
  Water Resources: Iran has limited freshwater resources, with 92.2% used in agriculture.
  Agricultural Efficiency: Iran's agricultural productivity is low compared to similar climates.
Internet of Things (IoT) in Agriculture
  IoT Definition: IoT consists of interconnected devices that communicate and collect data to optimize operations.
  Application: In agriculture, IoT is used for smart irrigation, machinery control, and livestock tracking.
16/32

## Slide 17
20-40%
Reduction of water consumption
20%
Increases agricultural yields
Smart Irrigation System
Technology: Utilizes Wireless Sensor Networks (WSNs) to monitor soil moisture, temperature, and weather conditions.
17/32

## Slide 18
Economic Impact on GDP
18/32

## Slide 19
Economic Impact on GDP
Table 2a and 2b
19/32

## Slide 20
Results and Discussion
  Implementation Cost: Approximately 1.05 billion Rials per hectare.
  Annual Costs: Calculated using investment data from pilot projects.
  Economic Benefits: Significant GDP growth due to improved agricultural efficiency and water savings.
20/32

## Slide 21
conclusion
  Potential for Economic Growth: IoT implementation in agriculture can lead to substantial economic benefits.
  Sustainable Water Use: Smart irrigation helps achieve sustainable water management.
  Recommendation: Promoting IoT adoption in agriculture to enhance productivity and economic stability.
21/32

## Slide 22
Evaluating the Possibility of Using the Power of the Received Signal to Estimate Soil Moisture
Case Study 2

## Slide 23
Paper Name: “Evaluating the Possibility of Using the Power of the Received Signal to Estimate Soil Moisture in Outdoor and Indoor Environments” (Original Name Is In Persian)
Three researchers from the Persian Gulf University have proposed a scientific approach based on Internet of Things (IoT) technology for measuring soil moisture.
The results indicate that with proper processing of the received signal strength indicator (RSSI), it is possible to estimate soil moisture in agriculture with acceptable accuracy.
This and the method proposed could lead to a massive reduction in expenses of implementing a system to control soil moisture in order to achieve excellent irrigation.
23/32

## Slide 24
Power Supply
Large Farms
Financial
Soil Moisture Measurement Challenges
24/32

## Slide 25
Experiment Methodology
Materials:
  a Lora module
  a soil moisture sensor
The experiment was conducted in both indoor (inside a building) and outdoor (on the campus of Persian Gulf University) environments..
25/32

## Slide 26
Results and Discussion
Indoor Environment
RSSI over time for indoor environment
26/32

## Slide 27
Results and Discussion
Indoor Environment
Soil moisture versus RSSI scattering for dry soil at night
Soil moisture versus RSSI scattering for wet soil at night
27/32

## Slide 28
Results and Discussion
Indoor Environment
Soil moisture versus RSSI scattering for dry soil at daylight
Soil moisture versus RSSI scattering for wet soil at daylight
28/32

## Slide 29
Results and Discussion
Outdoor Environment
RSSI over time for outdoor environment
29/32

## Slide 30
Conclusion
Ultimately, this research concludes that the relationship between RSSI and soil moisture is significant enough to consider it as an acceptable criterion for measuring and estimating soil moisture in smart agriculture at a much lower cost than similar methods.
30/32

## Slide 31
Email address
kianamahdian2002@gmail.com
yasmiintte@gmail.com
mahdielmaximo@gmail.com
Telegram
@kiacola
@yethereweare
@yacmin
Contact Us
31/32

## Slide 32
Resources
  Abbasi M. & Yaghmaee M. (2019). “Internet of Things In Agriculture: A Survey” University of Isfahan IoT Conference (2019)
  FaghihKhorasani H. & FaghihKhorasani A (2022). “Predicting the Impact of the Internet of Things on the Value Added for the Agriculture Sector In Iran Using Mathematical Methods” AGRIS on-line Papers in Economics and Informatics
  Dokard A., Keshavarz A. & Mansorinejad M. (2023). "Evaluating the Possibility of Using the Power of the Received Signal to Estimate Soil Moisture in Outdoor and Indoor Environments" University of Isfahan IoT Conference (Fall of 2023)
32/32

## Slide 33
Thank You!
4/32